## Slide 1: Master Thesis
cand. el. Dinggen Dai
Evaluation of Image-Based Approaches
Extracting a Mandrel’s Borders Using Machine Vision
Benedikt Haas

## Slide 2: Structure
1 Motivation and Objective
2 Concept
3 Methods
4 Result and Evaluation
5 Conclusion and Outlook

## Slide 3: 1 Motivation and Objective
Cardiovascular diseases caused 338,000 deaths [1]
  22.3% due to narrowing of heart disease vessels
Treatable by stent implementation [2]
Stent quality control in manufacturing is essential
  manual inspection VS. automatic inspection
Chart: Causes of death in Germany 2020
| Cardiovascular diseases | Cancers | Respiratory system diseases | Mental and behavioral disorders | Others
Causes of death | 338000 | 239600 | 61300 | 59322 | 294767
Stent implementation process [2]

## Slide 4: Motivation: Stent4Tomorrow
manufacturing system [3]
visual inspection related parts
of the system [3]
focus on the stent

## Slide 5: Objective: Borders extraction
Issue 1: the pitch size
  how to “enlarge”?
Issue 2: the background useless
  how to remove?
Solution: borders extraction!
Extra: the diameter of the mandrel already known (in mm)
  calculate the distance of the borders
  build mapping relations between image (in pixel) and human perception (in mm)

## Slide 6: 2 Concept
Assumption:
  the border lines are vertical to the x-axis of image
Input: RGB image
Output: two border lines
Metrics:
  1. RSE (root square error):
  2. Execution time
d1
d2
x
y

## Slide 7: Concept: diagram

## Slide 8: 3 Methods: Dataset
Original Image (RGB):
  size: 2064*3088*3 ( > 5 MB )
The labels:
  two border lines vertical to the x-axis
  format: [x_left_border, x_right_border]
Dataset splitting:
 | Training | Validation | Test
Total | 5529 | 1224 | 1694
Usable1 | 4881 | 1085 | 1508
Chart: 
| train | valid | test
dataset splitting | 4881 | 1085 | 1508

## Slide 9: Method: classic image process
Step 1. edge detector
  Bottom-up approachs:
    LSD (2010): still typical today [4]
    EDLines (2011): 10 times faster than LSD [5]
    CannyPF (2015): parameter free [6]
  Top-down approachs: based on hough transformation
    MCMLSD (CVPR 2017) [7]
Step 2. valid edge extractor
  filter: moving window
Step 3. border line generator
  least square method

## Slide 10: Method: deep learning
HT-LCNN (ECCV 2020) [8]
  based on LCNN (ICCV 2019)
  add a trainable Hough transfrom block into a deep network
F-Clip [9]
  SOTA of line detectors (2021)
  one stage: much more faster
  the representation of a line
An overview of LCNN architecture
An overview of F-Clip architecture

## Slide 11: 4 Result & Evaluation
Without MCMLSD

## Slide 12: Evaluation: RSE
Chart: Approches
| LSD | CannyPF | EDLines | MCMLSD | HT-LCNN | F-Clip
mean RSE | 28.8 | 35.8 | 108.8 | 50.9 | 19.77 | 20.52
Classic image process: LSD

## Slide 13: Evaluation: RSE
LSD: 2 kinds of bad cases
Case 1: no edge detected around the borders
Case 2: noise (stent wire) around the left border

## Slide 14: Evaluation: RSE
Deep learning: HT-LCNN

## Slide 15: Evaluation: RSE
HT-LCNN: the predicted left border line in the left side of the labeled

## Slide 16: Evaluation: execution time
Chart: Approches
| LSD | CannyPF | EDLines | MCMLSD | HT-LCNN | F-Clip
execution time | 340 | 338 | 88 | 20557 | 583 | 32
Chart: Approches
| LSD | CannyPF | EDLines | HT-LCNN | F-Clip
execution time | 340 | 338 | 88 | 583 | 32
Without MCMLSD

## Slide 17: 5 Conclusion and outlook
Conclusion:
  Implemented / reproduced 6 approches to detect the border lines
    4 in classic image process: LSD, EDLines, CannyPF, MCMLSD
    2 in deep learning: HT-LCNN, F-Clip
  Metric RSE:
    DL models show better performance: more robust to the noise
    Lowest of all: HT-LCNN 19.77 pixels
    Lowest of classic methods: LSD 28.8 pixels
  Metric execution time: F-Clip is the fastest with 32 (ms / image)
Outlook:
  Classic image process: based on LSD, deal with the two bad cases (robust to noise)
  Deep learning: try to use two junctions to represent a border line instead of the vertical line
    compared to the top point of the left border (obstruction from the background), easy to percept for human being

## Slide 18: Thank you for your attention!

## Slide 19: Appendix - Reference
[1]