## Slide 1: Master Thesis
cand. el. Dinggen Dai
Evaluation of Image-Based Approaches
Extracting a Mandrel’s Borders Using Machine Vision
Benedikt Haas

## Slide 2: Structure
1 Motivation and Objective
2 Concept
3 Methods
4 Result and Evaluation
5 Conclusion and Outlook

## Slide 3: 1 Motivation and Objective
Cardiovascular diseases caused 338,000 deaths [1]
  22.3% due to narrowing of heart disease vessels
Treatable by stent implementation [2]
Stent quality control in manufacturing is essential
  manual inspection VS. automatic inspection
Chart: Causes of death in Germany 2020
| Cardiovascular diseases | Cancers | Respiratory system diseases | Mental and behavioral disorders | Others
Causes of death | 338000 | 239600 | 61300 | 59322 | 294767
Stent implementation process [2]

## Slide 4: Motivation: Stent4Tomorrow
manufacturing system [3]
visual inspection related parts
of the system [3]
focus on the stent

## Slide 5: Objective: Borders extraction
Issue 1: the pitch size
  how to “enlarge”?
Issue 2: the background useless
  how to remove?
Solution: borders extraction!
Extra: the diameter of the mandrel already known (in mm)
  calculate the distance of the borders
  build mapping relations between image (in pixel) and human perception (in mm)

## Slide 6: 2 Concept
Assumption:
  the border lines are vertical to the x-axis of image
Input: RGB image
Output: two border lines
Metrics:
  1. RSE (root square error):
  2. Execution time
d1
d2
x
y

## Slide 7: Concept: diagram

## Slide 8: 3 Methods: Dataset
Original Image (RGB):
  size: 2064*3088*3 ( > 5 MB )
The labels:
  two border lines vertical to the x-axis
  format: [x_left_border, x_right_border]
Dataset splitting:
 | Training | Validation | Test
Total | 5529 | 1224 | 1694
Usable1 | 4881 | 1085 | 1508
Chart: 
| train | valid | test
dataset splitting | 4881 | 1085 | 1508

## Slide 9: Method: classic image process
Step 1. edge detector
  Bottom-up approachs:
    LSD (2010): still typical even now
    EDLines (2011): 10 times faster than LSD
    CannyPF (2015): parameter free
  Top-down approachs: based on hough transformation
    MCMLSD (CVPR 2017)
Step 2. valid edge extractor
  filter: moving window
Step 3. border line generator
  least square method

## Slide 12: Appendix - Reference
[1]

## Slide 13: Masterfolie (über: Ansicht – Master – Folienmaster)
Die Masterfolie wird genutzt, um grundlegende Elemente der Präsentation festzulegen und ggf. zu ändern.
Folgende Elemente können Sie in der Normalansicht individuell eintragen:
  Inhaltsbereich:
    Präsentationsüberschrift
    Unterüberschrift
    Fakultätsbezeichnung
    Bildaustausch (graue Lasche am rechten Folienrand – zum leichteren Austausch)
  Fußzeile (über: Ansicht – Kopf- und Fußzeile)

## Slide 14: Folientitel: Arial 24pt fett 2-zeilig: Arial 20pt fett
Fließtext: Arial 24pt regular
Fußzeile: Arial 9pt regular
Seitenzahl: Arial 9pt fett
Aufzählungspunkte, falls nicht auf Folie vorhanden:
  Format – Nummerierung- und Aufzählungszeichen – Bild – Importieren
  Die Datei „kit-point.png“ auswählen
  Größe: „70% vom Text“
Farben:
  Sind bereits voreingestellt. Sie erhalten automatisch die KIT-Farbpalette

## Slide 15: Generelle Hinweise
Das Foliendesign sollte nicht geändert werden
Wenn Sie aus einem anderen Office-Programm Texte kopieren, wird Powerpoint die Formatierungen beibehalten. Hier müssen Sie die Texte evtl. neu formatieren.
Grundlegende Elemente wie diese im grauen KIT-Rahmen, das KIT-Logo oder die Platzhalter sollten in der Position nicht verändert oder gelöscht werden.

## Slide 16: Tipps zur Verwendung von Powerpoint
Seitenaufbau
  Text und Grafiken: Diese Elemente sollten gezielt und zurückhaltend eingesetzt werden. Empfohlen werden zehn Worte pro Zeile und fünf Zeilen pro Folie.
  Zahlen und Daten Effektive PowerPoint-Präsentationen enthalten wenig Zahlen: ausführliche Daten können Sie nach der Präsentation auf Handouts verteilen.