## Slide 1: Master Thesis
cand. el. Dinggen Dai

## Slide 2: Structure
1 Motivation and Objective
2 Fundamental
3 Concept
4 Evaluation and Analyse
5 Conclusion and Outlook

## Slide 3: 1.1 Motivation: background
Stent: an important life-saving device
  treat cardiovascular diseases [1-2]
Stent manufacture:
  quality inspection: manual vs. Automatic
    high precision
    faster
    lower cost
Automatic inspect system is desirable!
Chart: Causes of death in Germany, 2020 [1]
| Cardiovascular diseases | Cancers | Respiratory system diseases | Mental and behavioral disorders | Others
Causes of death | 338000 | 239600 | 61300 | 59322 | 294767
Stent implantation process [2]

## Slide 4: 1.1 Motivation: background (Stent4Tomorrow)
manufacturing system [3]
visual inspection related parts [3]
focus on the stent

## Slide 5: 1.2 Objective: borders extraction
Issue 1: the size of the pitch
  how to “enlarge”?
Issue 2: the background
  single image size (3 ~ 8 MB)
  how to remove?
    less calculation
Solution: borders extraction!
Extra: build the mapping relations between image (pixel) and human perception (mm)
  1. the diameter of the mandrel already known (in mm)
  2. calculate the distance of the borders (in pixel)
focus on the stent

## Slide 6: Structure
1 Motivation and Objective
2 Fundamental
3 Concept
4 Evaluation and Analyse
5 Conclusion and Outlook

## Slide 7: 2 Fundamental: research domain
Why choose LSD (line segment detection)？
  straightforward
Part I: classic image process
  4 approaches
Part II: deep learning based
  2 approaches
Rome
Segmentation
Bounding box based object detection
……
……
LSD

## Slide 8: 2.1.1 Classic: bottom-up
LSD: line segment detector (2010) [4]
  now: still typical
EDLines (2011) [5]
  10 times faster than LSD

## Slide 9: 2.1.1 Classic: bottom-up
CannyPF (2015) [6]
  based on canny filter
  parameter free
(没有示意图)

## Slide 10: 2.1.1 Classic: bottom-up
LSD
EDLines
CannyPF

## Slide 11: 2.1.2 Classic: top-down
MCMLSD (CVPR 2017) [7]
Step1: HT
Step2: MCM

## Slide 12: 2.2 Deep learning (HT-LCNN 标注输出)
HT-LCNN (ECCV 2020) [8]
  based on LCNN (ICCV 2019)
  add a trainable Hough transfrom block into a deep network
F-Clip [9]
  SOTA of line detectors (2021)
  one stage: much more faster
  the representation of a line
An overview of LCNN architecture
An overview of F-Clip architecture

## Slide 13: 2.3 Input: Dataset
The image (RGB):
The labels:
  assumption:
    the border lines are vertical to the x-axis of image
  two numbers:
    x1: x-coordinate of the left border
    x2: x-coordinate of the right border
Dataset splitting:
 | Training | Validation | Test
Total | 4881 | 1085 | 1508
Chart: 
| train | valid | test
dataset splitting | 4881 | 1085 | 1508
x
y
x1
x2

## Slide 14: 2.4 Output: two border lines
Evalutation metrics:
  1. RSE (root square error):
  2. execution time
d1
d2
x
y
x1
x2

## Slide 15: Structure
1 Motivation and Objective
2 Fundamental
3 Concept
4 Evaluation and Analyse
5 Conclusion and Outlook

## Slide 16: 3.1 Concept: classic approaches
Start
Load RGB image
Border line generator
End
Get border lines
Valid edge extractor
Edge detector

## Slide 17: 3.1 Concept: classic approaches
Start
Load RGB image
Border line generator
End
Get border lines
Valid edge extractor
Edge detector

## Slide 18: 3.1 Concept: classic approaches
Start
Load RGB image
Border line generator
End
Get border lines
Valid edge extractor
Edge detector
angle filter + moving window

## Slide 19: 3.1 Concept: classic approaches
Start
Load RGB image
Border line generator
End
Get border lines
Valid edge extractor
Edge detector
  least square method

## Slide 20: 3.2 Concept: deep learning approaches
Start
Load RGB image
Head: line prediction
End
Get border lines
Head: multitask learner
Backbone
Model:

## Slide 21: Structure
1 Motivation and Objective
2 Fundamental
3 Concept
4 Evaluation and Analyse
5 Conclusion and Outlook

## Slide 22: 4.1 Evaluation metric: execution time
MCMLSD 打叉
Chart: Approches
| LSD | CannyPF | EDLines | MCMLSD | HT-LCNN | F-Clip
execution time | 340 | 338 | 88 | 20557 | 583 | 32
Chart: Approches
| LSD | CannyPF | EDLines | HT-LCNN | F-Clip
execution time | 340 | 338 | 88 | 583 | 32

## Slide 23: 4.2 Evaluation metric: mean RSE (root square error)
概览分布
  Classic：选择LSD
  DL：选择HT-LCNN
LSD为例，但是classci都有这个问题 general issues
Chart: Approches
| LSD | CannyPF | EDLines | MCMLSD | HT-LCNN | F-Clip
mean RSE | 28.8 | 35.8 | 108.8 | 50.9 | 19.77 | 20.52

## Slide 24: 4.2 Evaluation metric: mean RSE
Classical image processLSD为例，但是classci都有这个问题 general issues

## Slide 25: 4.2 Evaluation metric: mean RSE
LSD: 2 kinds of bad cases
Case 1: no edge detected around the borders
Case 2: noise (stent wire) around the left border

## Slide 26: 4.2 Evaluation metric: mean RSE
Deep learning: HT-LCNN

## Slide 27: 4.2 Evaluation metric: mean RSE
HT-LCNN: the predicted left border line in the left side of the labeled

## Slide 28: 4.3 Evaluation summary

## Slide 29: Structure
1 Motivation and Objective
2 Fundamental
3 Concept
4 Evaluation and Analyse
5 Conclusion and Outlook

## Slide 30: 5 Conclusion and outlook
Conclusion:
  Implemented / reproduced 6 approaches
  Metric mean RSE:
    DL models show better performance: more robust to the noise
    Lowest of all: HT-LCNN 19.77 pixels
    Lowest of classic methods: LSD 28.8 pixels
  Metric execution time: F-Clip is the fastest with 32 (ms / image)
Outlook:
  Classic image process: based on LSD, deal with the two bad cases (robust to noise)
  Deep learning: try to use two junctions to represent a border line instead of the vertical line
    compared to the top point of the left border (obstruction from the background), easy to percept for human being

## Slide 31: Thank you for your attention!
Start
Load RGB image
Border line generator
End
Get border lines
Valid edge extractor
Edge detector
Start
Load RGB image
Head: line prediction
End
Get border lines
Head: multitask learner
Backbone

## Slide 32: Appendix - Reference
[1]